## Slide 1
Proofs for Masking Schemes
Sebastian Faust
Ruhr University Bochum

## Slide 2
Cryptodevices
cryptographic device
implementation
very secure
much less secure!
well-defined mathematical object
often proofs of security
many ways of implementing: details matter!
new attacks possible on crypto implementations
One reason: models of provable security do not capture many relevant implementation attacks

## Slide 3
Theory vs. Reality
Black box model:
Controls inputs /outputs but internals stay hidden
Attack Implementation:
KEY
Devices leak about internals
implement
Best attack for AES practically impossible
Can break AES within days with side-channel analysis

## Slide 4
Proofs for implementations
Include leakage into black-box model
Devise new schemes and prove their security
Many examples: encryption, signatures, authentication
a) Specific schemes
Leakage resilient circuits
b) Arbitrary computation
Why leakage resilient circuits?
1. Theoretical feasability: computation under leakage
2. Practically relevant: masking countermeasure

## Slide 5
Leakage resilient circuits

## Slide 6
Leakage resilient circuits
Masking

## Slide 7
Important countermeasure
Masking: Protect all intermediate values of computation with randomized encoding Enc
Description of algorithm, e.g., AES
K’
C’
C
K
Computes AES on encoded values
Harder to exploit leakage from protected algorithm
Robust encoding function
Two ingredients of a masking scheme
Leaks less about k
K
Enc(K)

## Slide 8
Important countermeasure
Masking: Protect all intermediate values of computation with randomized encoding Enc
Description of algorithm, e.g., AES
K’
C’
C
K
Computes AES on encoded values
Harder to exploit leakage from protected algorithm
Robust encoding function
Operations computing with encoded values
Two ingredients of a masking scheme
Enc(X)
Enc(Y)
Enc(X*Y)
Compute on encoded values

## Slide 9
Leakage resilient circuits
Circuit Compiler

## Slide 10
Leakage resilient circuits
C
K
X
Formalization of masking by Ishai-Sahai-Wagner-03
Y
Arbitrary computation modeled as a circuit

## Slide 11
Leakage resilient circuits
K’
C’
C
K
Circuit compiler
X
Formalization of masking by Ishai-Sahai-Wagner-03
How to formalize this?
Y
X
Y
Circuit Compiler: Run once at production time (no leakage)
Input: Description of circuit C with key K (e.g., circuit for AES)
Output: Description of circuit C’ with key K’ (C’ is probabilistic)
Correctness: C[K] and C’[K’] have same functionality
Additionally: C’[K’] leakage resilient for many executions
 adversary learns nothing “useful” from leakage
?

## Slide 12
Real:
K’
C’
C
K
X
Y
Simulation-based security
X,
f
Y, f(state)
indistinguishable
output
output
Repeat many times
Continuous leakage: many observations are possible
What function can the leakage f be?
Ideal:
Adversary learns no more than by black-box access
What does it mean?
For unbounded adversary: MI(K ; f(.), ... f(.)) < negl
Even more: Cannot break underlying security notion
Notes: Write state in leakage function

## Slide 13
Leakage resilient circuits
t-probing model

## Slide 14
n-Probing adversary (ISW03)
Adversary gets t intermediate values of computation
 L = { values on t adversarial chosen wires }
t-probing attack formalization of t-variate attacks
Basic ingredient: Additive masking
K := (K1…Kn) s.t. K=K1+...+ Kn
K
Encode
C
M
●
+
●
…
Learns nothing if t < n
How to compute with additive encodings?

## Slide 15
ISW Compiler: High level
1. Memory:
A bit s
K’
C’
C
K
a
s
s’
and
and
and
output
neg
A
S
S’
and
C s.t. Dec(C)=a∧s
C s.t.Dec(C)=s∧s’
Dec
Enc
a
output
and
D
and
neg
Encoded with additive masking, i.e., S = (S1…Sn) such that
s = S1 + … + Sn
Notes: Recall…

## Slide 16
K’
C’
C
K
a
s
s’
and
and
and
output
neg
A
S
S’
and
C s.t. Dec(C)=a∧s
C s.t.Dec(C)=s∧s’
Dec
Enc
a
output
and
D
and
neg
ISW Compiler: High level
2. Wires:
Each wire
w = a ∧ b
Wire bundle carrying encoding C such that w = Dec(C)
Main challenge: computing on encoded inputs!

## Slide 17
a
s
s’
and
and
and
output
neg
A
S
S’
and
C s.t. Dec(C)=a∧s
C s.t.Dec(C)=s∧s’
Dec
Enc
a
output
and
D
and
neg
ISW Compiler: High level
3. Gates:
Gadgets built from standard gates operating on encodings
Main challenge: algorithm to securely compute AND!
*

## Slide 18
Theorem: A compiler that makes any circuit resilient to adversary that probes up to n wires in C’
ISW Compiler: Results
K’
C’
C
K
Blow-up in size: O(n2) for each AND gate in C
Leakage bounded per observation: t < n wires
Drawback: L only probing  oblivious of many wires
Proofs in n-probing model: Systematic and simple tool to find n-th variate flaws in masking schemes
Barthe et al. EC15: Automated tool to verify proofs

## Slide 19
Leakage resilient circuits
More powerful leakages

## Slide 20
New model for circuits
input
output
Bounded independent leakages
L
R
Assumption: Processors leak independently!
f(L,T)
g(R,T)
T
Processors can communicate with each other –
Think of it as a 2-party protocol!
Circuit C’
 Everything that is touched on a processor leaks!
Additive masking? Insecure: learn parities of L & R
Realistic? Includes many functions, e.g. weighted sums
m bits
f
- Arbitrary efficient functions
- Ony restriction: input shrinking, i.e., c < m
c bits
Bounded leakage function:

## Slide 21
Inner Product Masking
Sample L,R uniformly in {0,1}n s.t. S= <L,R> = Σ Li*Ri and store parts separately on two processors
n
n
R
L
f(L)
g(R)
?
Thm [DDV10]: if leakage is bounded in total to c bits then adversary learns nothing about S
L
R
Extract
̴̴̴ uniform
High min-entropy and independent sources

## Slide 22
IP Compiler: High level
1. Wires and state is encoded using IP masking
K’
C’
C
K
a
S
S’
and
and
and
output
neg
(L,R)
(L’,R’)
(L’’,R’’)
and
(L,R) s.t. <L,R>=a∧S
(L,R) s.t. <L,R>=S∧S’
Dec
Enc
a
S
S’
output
and
(L,R)
and
neg
2. Gates are replaced by protocols working on IP masking
 Most difficult: protocol to compute AND

## Slide 23
Outline: MULT operation…
Input: encoding (L,R) of S and (L’,R’) of S’
Notice: L,L’ and R,R’ each hold by one player
L
L’
R
R’
L’’
R’’
S’
S
S’’
Output: securely compute encoding (L’’,R’’) of S*S’

## Slide 24
An observation
* | L1 | L2 | L3
L'1 | L1L'1 | L2L'1 | L3L'1
L'2 | L1L'2 | L2L'2 | L3L'2
L'3 | L1L'3 | L2L'3 | L3L'3
R1 | R2 | R3 | *
R1R'1 | R2R'1 | R3R'1 | R'1
R1R'2 | R2R'2 | R3R'2 | R'2
R1R'3 | R2R'3 | R3R'3 | R'3
L1L'1
L1L'2
L1L'3
L2L'1
L2L'2
L2L'3
L3L'1
L3L'2
L3L'3
R1R'1
R1R'2
R1R'3
R2R'1
R2R'2
R2R'3
R3R'1
R3R'2
R3R'3
A :=
=: B
L
L’
*
*
*
R
R’
<A,B> = <L,R> * <L’,R’> = S*S’
Easy calculation:
L
L’
R
R’
S’
S

## Slide 25
Outline: MULT operation…
A
L’’
R’
Computes locally:
Computes locally:
 | L1 | L2 | L3
L'1 | L1L'1 | L2L'1 | L3L'1
L'2 | L1L'2 | L2L'2 | L3L'2
L'3 | L1L'3 | L2L'3 | L3L'3
R1 | R2 | R3 | 
R1R'1 | R2R'1 | R3R'1 | R'1
R1R'2 | R2R'2 | R3R'2 | R'2
R1R'3 | R2R'3 | R3R'3 | R'3
B
L
L’
R
R’’
<A,B> = S * S’
the length of A and B is quadratic in n!
protocol
Provably secure protocol in [DF12]

## Slide 26
The IP masking compiler
x
Theorem:
A new information theoretic secure compiler with security against continuous independent leakage
K’
C’
C
K
Blow-up in size: O(n2) for each AND gate in C
IP masking in practice?
Leakage bounded per exec.: c bits from each processor

## Slide 27
Leakage resilient circuits
IP masking in practice

## Slide 28
IP Masking in practice? (BFGV12, BFG15)
Analyzed for small security parameter n –
Security outperforms Boolean masking
Main reason: Non-linear masking vs. linear masking
Mutual information between HW leakage and secret
Weaker dependency between leakage & secret for IP masking
x
Green curve: Boolean masking with 3 random shares in GF(28)
Red curve: IP masking with 3 random shares in GF(28)
Performance: Runs AES in 300k clock cycles for n=2
Use squaring whenever possible  it’s cheap!
Efficient implementations for add and multiplication

## Slide 29
Leakage resilient circuits
Noisy leakages

## Slide 30
Bounded leakage?
Models do not match with my engineering experience
Leakages are not quantitatively bounded
Beautiful theory! Q: Does it match practice?
Physical leakages are inherently noisy
Difficulty in many attacks: how to eliminate the noise?

## Slide 31
Noisy leakages – Chari et al. 99
No quantitative bound on leakage, but leakage is noisy
b1
b2
…
...
bn
For bit b: Enc(b)
...
Leakage is bi + Gaussian noise
Chari et al. only consider security of a single masked bit
p-noisy functions N(.): More general noise distribution [PR13]
X0, X1
uniform
2. N(Xb)
N(X0), X0, X1
N(X1), X0, X1
1. b {0,1}
≈
N is p-noisy if statistical distance < p

## Slide 32
Pr[Noise(x)=y]
Noise(x)=y
 Adv. learns Noise(bi): full knowledge about secret b
Some examples ( F = GF(2) )
No noise p ≈ 1: very informative leakage
Pr[Noise(1)=y]
y
Pr[Noise(0)=y]
y
 Adv. learns Noise(bi): no knowledge about b
High noise p = 0: non-informative leakage
Encoding insecure
Enc secure
Noise(0)
Noise(1)
Notes: Finite field

## Slide 33
Pr[Noise(x)=y]
Noise(x)=y
Some examples ( F = GF(2) )
Interesting case: „some noise“
 Adv. learns Noise(bi): knowledge about b decreases exponentially in n
For p < 1/8 and sufficiently large n:
How about leakage from computation?
Notes: Finite field

## Slide 34
Circuits for noisy leakage [PR13, DDF14]
x
K’
C’
C
K
Compiler of ISW03
Adversary obtains noisy version of each wire: N(wi)
Two proof techniques:
Direct proof: very technical proof, only random message security
Reduction to probing model: simple proofs, full simulation-based security
No quantitative bound on amount of leakage

## Slide 35
Main observation
secret
Leakage
Noisy leakage
Probing leakage
equivalent
C
M
●
+
●
Simpler model than bounded leakage
Preferred model in practice
How to prove equivalence:
1. Simpler noise model: random probing
2. Random probing = noisy leakages
 Simulate noisy leakage with random probing

## Slide 36
Proof outline
Random probing model (ISW03)
C1
C2
…
...
Cn+1
f(Ci) = Ci with prob. q; otherwise f(Ci) = „?“
...
f(C1)
f(C2)
f(Cn+1)
Adv. learns S only if „lucky“ in each random probe
Encoding secure in random probing model for constant q
Notes: Write state in leakage function

## Slide 37
Proof outline
For any x and Noise(.) there exists Noise‘(.) such that Noise(x) = Noise‘(f(x))
Random probing  noisy leakage
First extreme case: “no noise” (p≈1)
Noise(0)
Noise(1)
No way to “simulate” this noise except with random probing where q=1 (i.e., reveals everything).
Notes: Finite field

## Slide 38
Proof outline
For any x and Noise(.) there exists Noise‘(.) such that Noise(x) = Noise‘(f(x))
Random probing  noisy leakage
Second extreme case: “full noise” (p=0)
Set Noise‘ = Noise: Simulation is possible without even probing: q = 0 (i.e., reveals nothing)
Noise(0) and Noise(1)
are identical
Notes: Finite field

## Slide 39
Proof outline
Interesting case: “some noise”
If f(x) = ?  sample y according to
min(Pr[N(0)=y], Pr[N(1)=y]) (normalized)
If f(x) =1
(similar)
Noise(0)
Noise(1)
If f(x) =0  Pr[N(0) =y] –
Pr[N(1)=y] (normalized)
One can “simulate” Noise(.) with random probing when probability q is exactly Δ(Noise(0),Noise(1))
(proof is essentially a simple „averaging argument“)
Notes: Finite field

## Slide 40
Leakage resilient circuits
Conclusion

## Slide 41
Conclusion
 Proofs in n-probing model to check for n-th order flaws
Why proofs for masking?
Systematic analysis to avoid flaws
New ideas and schemes
Formal requirements on hardware
 IP masking an alternative for additive masking?
 How much noise do I need to use masking?
Many open questions
Better models
Better efficiency
Dependency, glitches,
better bounds...
O(n) complexity also for small circuits

## Slide 42
Thank you!