## Slide 1: Resource-efficient Cryptography for Ubiquitous Computing
Elif Bilge Kavun
Summer School on Real-world Crypto and Privacy
20.06.2019, Šibenik

## Slide 2: Outline
Why do we need it?
Initial proposals
Proposals addressing certain metrics
Side-channel resistance?

## Slide 3: Ubiquitous Computing Era

## Slide 4: Ubiquitous Computing Era

## Slide 5: Ubiquitous Computing Era

## Slide 6: Ubiquitous Computing Era
Embedded devices everywhere!
Electronic passports
Automation components
Asset tracking systems
Payment and toll-collection cards
RFID tags
Smart cards
…

## Slide 7: Ubiquitous Computing Era
Security Concerns
Car key systems
Medical & sensor systems
Smart home
Access control
Security
Privacy protection
…
Notes: More information:
You can crop a picture (trim slices from the side, top or bottom) by selecting on the slide the picture that you want to crop, going to the “format” menu, selecting “picture…” and in the “picture” dialog box clicking the “picture” button. This opens the crop options. The preview button allows you to see whether the crop achieves the effect you wanted. (If you have an old version of PowerPoint these controls may be located differently - refer to the PowerPoint Help menu.)
Before importing a picture into your presentation save it in a suitable format (eg jpeg) at a resolution of 72 dots per inch if possible. This resolution keeps the size of the picture file small but still displays fine on screen – particularly important if you’re using several pictures, because half a dozen taken on a five megapixel digital camera and imported at full resolution could mean that your presentation is over 20 megabytes in size. This means it will take up unnecessary disk space, will be slow to open and run on many less powerful computers – and will be too big to e-mail.

## Slide 8: Ubiquitous Computing Era
Good security architectures needed
to resist these attacks!

## Slide 9: Need for Security: Same level?
Embedded devices are resource-constrained!
  Circuit size, ROM/RAM sizes
  Power
  Energy
    Battery-driven devices
  Processing speed: Throughput, delay
    Large data transmissions
    Real-time control processing

## Slide 10: Need for Security: Same level?
Conventional cryptography
  Servers
  Desktops
  Tablets
  Smartphones

## Slide 11: Need for Security: Same level?
Tailored cryptography for
  Embedded systems
  RFIDs
  Sensor networks

## Slide 12: Need for “Tailored” Cryptography
Lightweight cryptography!

## Slide 13: Need for “Tailored” Cryptography
Resource-efficient cryptography!

## Slide 14: What is resource-efficient cryptography?
Reduces computational efforts to provide security
  Less expensive than traditional crypto
  Not weak, but “sufficient„ security
    Reduced level – key size generally below 128 bits

## Slide 15: What is resource-efficient cryptography?
Many proposals/implementations so far
  Public-key cryptography: ECC, NTRU, …
  Stream ciphers: Grain, Trivium, …
  Hash functions: Photon, Quark, …
  Block ciphers
    Core for symmetric crypto, stream ciphers, MAC, etc

## Slide 16: Resource-efficient Block Ciphers
Solutions both from industry and academia
  Industry
    In case of propriatery solutions, no public evaluation
    Generally efficient, but non-standard
    Lessons learned: MIFARE, Keeloq (stream cipher), etc attacks
  Academia
    Good solutions, but sometimes missing industry demands

## Slide 17: Resource-efficient Block Ciphers
AES: Standard cipher – but, lightweight?
  Actually not too bad for software implementations
  But expensive for hardware
    Serial implementations get close

## Slide 18: Resource-efficient Block Ciphers

## Slide 19: CLEFIA
By SONY
128-bit key minimum
Feistel network
Balancing security, speed, cost
Several Sboxes
ISO standard
Notes: More information:
You can crop a picture (trim slices from the side, top or bottom) by selecting on the slide the picture that you want to crop, going to the “format” menu, selecting “picture…” and in the “picture” dialog box clicking the “picture” button. This opens the crop options. The preview button allows you to see whether the crop achieves the effect you wanted. (If you have an old version of PowerPoint these controls may be located differently - refer to the PowerPoint Help menu.)
Before importing a picture into your presentation save it in a suitable format (eg jpeg) at a resolution of 72 dots per inch if possible. This resolution keeps the size of the picture file small but still displays fine on screen – particularly important if you’re using several pictures, because half a dozen taken on a five megapixel digital camera and imported at full resolution could mean that your presentation is over 20 megabytes in size. This means it will take up unnecessary disk space, will be slow to open and run on many less powerful computers – and will be too big to e-mail.

## Slide 20: Resource-efficient Block Ciphers

## Slide 21: PRESENT
Targeting hardware
Simple but strong design
  Well-studied substitution-permutation network (SPN)
Low-area (permutation just wiring in hw!)
ISO Standard

## Slide 22: Resource-efficient Block Ciphers

## Slide 23: KLEIN
AES-like
Works on nibbles
Involution Sbox

## Slide 24: Resource-efficient Block Ciphers

## Slide 25: LED
AES-like
Uses PRESENT Sbox
Consists of steps (number based on key size)
  Each step 4 rounds

## Slide 26: Proposals vs Metrics
Initial proposals mostly address area
There are other important metrics
Security
Speed/Latency
Area/Power
Key/data size
Number of rounds
Implementation
(serial, round-based, unrolled)
Notes: More information:
You can crop a picture (trim slices from the side, top or bottom) by selecting on the slide the picture that you want to crop, going to the “format” menu, selecting “picture…” and in the “picture” dialog box clicking the “picture” button. This opens the crop options. The preview button allows you to see whether the crop achieves the effect you wanted. (If you have an old version of PowerPoint these controls may be located differently - refer to the PowerPoint Help menu.)
Before importing a picture into your presentation save it in a suitable format (eg jpeg) at a resolution of 72 dots per inch if possible. This resolution keeps the size of the picture file small but still displays fine on screen – particularly important if you’re using several pictures, because half a dozen taken on a five megapixel digital camera and imported at full resolution could mean that your presentation is over 20 megabytes in size. This means it will take up unnecessary disk space, will be slow to open and run on many less powerful computers – and will be too big to e-mail.

## Slide 27
 | Hardware | Software
Area/ Code size |  | ?
Latency/ Execution time | ? | ?
CLEFIA
PRESENT
HIGHT
KATAN
KTANTAN
mCrypton
TWINE
KLEIN
LED
LBlock
Piccolo
SIMON
ITUBee
KLEIN
SEA
SPECK
LBlock
TWINE
KLEIN
SPECK

## Slide 28
 | Hardware | Software
Area/ Code size |  | ?
Latency/ Execution time | ? | ?
CLEFIA
PRESENT
HIGHT
KATAN
KTANTAN
mCrypton
TWINE
KLEIN
LED
LBlock
Piccolo
SIMON
ITUBee
KLEIN
SEA
SPECK
LBlock
TWINE
KLEIN
SPECK
PRINCE

## Slide 29
 | Hardware | Software
Area/ Code size |  | ?
Latency/ Execution time | ? | ?
CLEFIA
PRESENT
HIGHT
KATAN
KTANTAN
mCrypton
TWINE
KLEIN
LED
LBlock
Piccolo
SIMON
ITUBee
KLEIN
SEA
SPECK
LBlock
TWINE
KLEIN
SPECK
PRINCE
PRIDE

## Slide 30: PRINCE: Towards Low-latency
Latency: Time to encrypt one block of data
single clock cycle: Unrolled design fashion
Moderate hardware costs
Encryption and decryption with low overhead
Graphics credit: Gregor Leander
Can we do better?

## Slide 31: PRINCE: Towards Low-latency
Latency: Time to encrypt one block of data
single clock cycle: Unrolled design fashion
Moderate hardware costs
Encryption and decryption with low overhead
Graphics credit: Gregor Leander
Can we do better?
Yes, we can!

## Slide 32: PRINCE: Key Figures
All rounds are unrolled
  Cipher can be thought as one big round
Try to keep the cost of one round as low as possible
All rounds same, decreases cost
Minimum overhead for encryption and decryption
  64-bit block, 128-bit key
  Core cipher with 64-bit key
  64-bit whitening keys
  12 rounds

## Slide 33: PRINCE: Key Figures
All rounds are unrolled
  Cipher can be thought as one big round
Try to keep the cost of one round as low as possible
All rounds same, decreases cost
Minimum overhead for encryption and decryption
  64-bit block, 128-bit key
  Core cipher with 64-bit key
  64-bit whitening keys
  12 rounds
  64-bit block, 128-bit key
  Core cipher with 64-bit key
  64-bit whitening keys
  12 rounds

## Slide 34: PRINCE: Core Cipher
  Middle part M’ is an involution linear layer
  M and M-1 are derived from M via ShiftRows operations
  S: 16 parallel applications of a 4-bit Sbox

## Slide 35: PRINCE: Round-based
  11 cycles instead of 12!

## Slide 36: PRINCE: Sbox
Optimize # of gate equivalents (GE) used by Sbox
  This is the main area saving
    But not necessarily same for serial implementations!

## Slide 37: PRINCE: Sbox
64000 Sboxes (and their inverses) with good cryptographic criteria are implemented and synthesized to obtain average gate counts
Smallest Sbox selected
  Area distribution of
  good Sboxes (90 nm)

## Slide 38: PRINCE: Area Results (kGE)
Chart: 
| PRINCE | PRESENT-80 | PRESENT-128 | LED-128 | AES-128 | CLEFIA-128* | HIGHT-128* | mCrypton-128* | Piccolo-128*
 | 8.3 | 50.4 | 55.5 | 109.7 | 118.4 | 28 | 42.7 | 37.6 | 25.7

## Slide 39: PRIDE: Target
A block cipher optimized for software implementations on widely-used embedded microprocessors
(e.g., Atmel ATmega8A)
  Benchmark
    SPECK-64/128 cipher of NSA* (also uses ATMega8A)
* Beaulieu et al, The Simon and Speck Families of Lightweight Block Ciphers, IACR ePrint Archive 2013/404, 2013

## Slide 40
PRIDE: Key Figures
Bitslicing idea used in design
  Brings additional permutation without any further effort
Substitution-permutation network
64-bit block, 128-bit key, 64-bit whitening keys
20 rounds
  Last round different – no diffusion as it is not necessary

## Slide 41: PRIDE: Design
Substitution-Permutation Network (SPN) adopted
  Well-understood

## Slide 42: PRIDE: Design
Linear layer: Expensive
One PRESENT round‘s linear layer cost:
  Just wiring (no cost) in hardware
  144 clock cycles in software (Atmel ATmega8A)

## Slide 43: PRIDE: Design
Block interleaving construction

## Slide 44: PRIDE: Bitslicing

## Slide 45: PRIDE: Bitslicing

## Slide 46: PRIDE: Bitslicing

## Slide 47
PRIDE: Bitslicing

## Slide 48: PRIDE: Bitslicing
…

## Slide 49: PRIDE: Bitslicing
…
Sbox: ANF
  a’ = fa(a, b, c, d)
  b’ = fb(a, b, c, d)
  c’ = fc(a, b, c, d)
  d’ = fd(a, b, c, d)

## Slide 50: PRIDE: Bitslicing
…
Sbox: ANF
  a’ = fa(a, b, c, d)
  b’ = fb(a, b, c, d)
  c’ = fc(a, b, c, d)
  d’ = fd(a, b, c, d)
Additional permutation

## Slide 51: PRIDE: Implementation View

## Slide 57
Permutation

## Slide 58
Sbox
Permutation

## Slide 59
Sbox
Permutation

## Slide 60
Sbox
Permutation

## Slide 61
Sbox
Permutation

## Slide 62
Sbox
Permutation

## Slide 63
Sbox
(formulation)
4-bit
involution

## Slide 64
Sbox
(formulation)
R0’ = R4 XOR (R0 AND R2)
R2’ = R6 XOR (R2 AND R4)
R4’ = R0 XOR (R0’ AND R2’)
R6’ = R2 XOR (R2’ AND R4’)
4-bit
involution
10 instructions

## Slide 65
Sbox
(formulation)
R0’ = R4 XOR (R0 AND R2)
R2’ = R6 XOR (R2 AND R4)
R4’ = R0 XOR (R0’ AND R2’)
R6’ = R2 XOR (R2’ AND R4’)
R1’ = R5 XOR (R1 AND R2)
R3’ = R7 XOR (R3 AND R5)
R5’ = R1 XOR (R1’ AND R3’)
R7’ = R3 XOR (R3’ AND R5’)
4-bit
involution
10 instructions
10 instructions

## Slide 66
Sbox
(formulation)
4-bit
involution

## Slide 67
Linear Layer

## Slide 68
Linear Layer
L0

## Slide 69
Linear Layer
L0
L1

## Slide 70
Linear Layer
L0
L1
L2

## Slide 71
Linear Layer
L0
L1
L2
L3

## Slide 72
Linear Layer
L0
L1
L2
L3
16 x 16 matrices!

## Slide 73
Linear Layer
L0
L1
L2
L3
16 x 16 matrices!
Should not be very costly: Look for efficiently implementable Li!

## Slide 74: PRIDE: How to Choose Li
Looking for “the cheapest implementation of a given linear layer L”?

## Slide 75: PRIDE: How to Choose Li
Looking for “the cheapest implementation of a given linear layer L”?
NO!
“Which good linear layer can be implemented with ‘N‘ minimum instructions”?
  In turn it gives us also...
    # of clock cycles for speed
    #of bytes for code size
Instead...

## Slide 76: PRIDE: How to Choose Li
Focus on smaller linear layers Li – Block interleaving helps!
  Reduces the search space
Search for ‘efficient‘ permutation matrices
  Look for 4 efficiently-implementable 16x16 binary permutation matrices
  Similar to Sbox search of Ullrich et al.*
    Search performed on hardware platform instead of software platform
    Faster search, larger search space
* Ullrich et al., Finding Optimal Bitsliced Implementations of 4 x 4-bit S-boxes, SKEW 2011

## Slide 77: PRIDE: Search on Hardware
8 x 8
Search in a subset of possible 16 x 16 matrices using an FPGA
  16 x 16 still quite large...
Li

## Slide 78
Limit number of instructions
  CLC, EOR, MOV, MOVW, CLR, SWAP, ASR, ROR, ROL, LSR, LSL
Limit number of used registers
  2 state, 4 temporary registers
Try all possible combinations of instructions and registers
Save the matrices generating appropriate code
  Out of these, look for the ones with least instructions
Ended up with 36 instructions for the whole linear layer!
  L0=7, L1=11, L2=7, L3=11, L0-1=7, L1-1=13, L2-1=7, L3-1=13

## Slide 79: PRIDE: Results
One Round Cost | Key Update | Key Addition | Sbox Layer | Linear Layer | Total
Time (Clock Cycles) | 4 | 8 | 20 | 36 | 68
Code Size (Bytes) | 8 | 16 | 40 | 72 | 136

## Slide 80
 | AES-128 | SERPENT-128 | PRESENT-128 | CLEFIA-128 | SEA-96 | NOEKEON-128 | PRINCE-128 | ITUBee-80 | SIMON-64/128* | SPECK-64/96* | SPECK-64/128* | PRIDE
Time (Clock Cycles) | 3159 | 49314 | 10792 | 28648 | 17745 | 23517 | 3614 | 2607 | 2000 | 1152 | 1200 | 1514
Code Size (Bytes) | 1570 | 7220 | 660 | 3046 | 386 | 364 | 1108 | 716 | 282 | 182 | 186 | 266
Performance on Atmel AVR 8- bit microcontroller (encryption)
  PRIDE decryption: 1570 clock cycles and 282 bytes
Results close to SPECK
  Good results for a “traditional” design
* Data & key read-write omitted

## Slide 81: Threshold Implementation: PRINCE
Bozilov et al (KU Leuven) at LWC Workshop 2016

## Slide 82
Applied on PRINCE Sbox: Algebraic degree 3, Class Q294
Unprotected, round-based PRINCE
Notes: Mention affine transformations.
Separating nonlinear operations means 3 clock cycles for single PRINCE Sbox call.

## Slide 83
Class Q294 sharing, first-order secure, 3 by 3 sharing
No re-masking, sharing is uniform

## Slide 84
Class Q294 sharing, second-order secure, 5 by 10 sharing
Re-masking applied

## Slide 85
PRINCE-128 (round-based implementation) unprotected
PRINCE-128 (round-based implementation) 1st-order secure
PRINCE-128 (round-based implementation) 2nd-order secure
Technology | Area (GE)
ASIC, 90nm | 3589
Technology | Area (GE)
ASIC, 90nm | 11958
Technology | Area (GE)
ASIC, 90nm | 21879
Notes: Results better than our back-the-envelope 1st order estimations (~20k)
No evaluation available.

## Slide 86: Side-channel Resistant Resource-efficient Block Ciphers

## Slide 87: Side-channel Resistant Resource-efficient Block Ciphers

## Slide 88: Side-channel Resistant Resource-efficient Block Ciphers

## Slide 89
Thanks for listening.
Any questions?