## Slide 1: Microarchitectural Weird Machines
Yuval Yarom
Ruhr University Bochum

## Slide 2: Publications
The Gates of Time: Improving Cache Attacks with Transient Execution
Daniel Katzman
William Kosasih
Chitchanok Chuengsatiansup
Eyal Ronen
Spec-o-Scope: Cache Probing at Cache Speed
Gal Horowitz
Eyal Ronen

## Slide 3: Emergent Behaviour

## Slide 4: Emergent Behaviour
Game of life
A cell is born if it has 3 neighbours; survives if it has 2 or 3.
Emergent behaviour:
  Unintended side effect of a system

## Slide 5: More examples
From: https://experiments.withgoogle.com/conway-game-of-life

## Slide 6: The memory wall
Processors are fast
Memory is slow
Slows execution when waiting for data
Cache: a small bank of fast memory Exploit locality to improve performance
Stores recently accessed data for quick future access
Processor
Memory
Cache
Notes: Another thing that changed since my Apple // days is the processor speed. My apple 2 ran at 1 MHz. My mac runs at 2GHz. Memory speed, however, has not fared so well. The memory on my apple needed half a clock cycle to produce data, whereas modern computers require about 200. When the processor reads from memory it needs to wait. <click> and if it needs to read from the same location again it needs to wait again. <click>. So, we have a speed gap between the processor and the memory.
The cache is the part of the processor that bridges this gap. It is a small memory that is included within the processor. Being small, being closer to the execution core and using more expensive technologies than the main memory mean that the cache is much faster than the memory. On intel the spead ranges from 4 to 50 cycles, depending on the level of cache.
Yada yada

## Slide 7: Cache operations
Accessing memory brings it to the cache
Flushing memory evicts it from the cache

## Slide 8: Emergent behaviour
Measuring access time tells us whether a location is cached or not

## Slide 9: Cache construction
Arranged as matrix
Memory locations mapped to sets
Can be stored in any of the ways of the set
Replacement policy decides where
Sets
Ways

## Slide 10: More Emergent Behaviour
Fill a cache set with data
Wait a bit
Measure access time to data
Can monitor other programs!

## Slide 11: Logical State of Cache
F F F T F F F F T F F F F
Associate a logical value with memory addresses
  TRUE – address is cached
  FALSE – address is not cached
Flushing sets a value to FALSE
Accessing memory sets a value to TRUE (may also set another to FALSE)
Measuring access time observes value (and set to TRUE)
What else?
Processor
Memory
Cache
F
T

## Slide 12: Conditional access
What is the cache state of *out after execution?
TRUE if *in != 0.
What if *in == 0?
if (*in == 0)
return;
out *= 1;
out *= 1;
a = *out
Assume *in == 0

## Slide 13: Speculative execution
if (*in == 0)
return;
out *= 1;
out *= 1;
a = *out
Evaluation of branch conditions can take time
The CPU predicts future execution
  Correct prediction – win
  Incorrect prediction – rollback
  Microarchitectural state remains
May be executed even if *in == 0
Assume
*in == 0
Assume branch mispredicted

## Slide 14: Conditional Speculative Execution
Assume
*in == 0
Branch mispredicted
if (*in == 0)
return;
out *= 1;
out *= 1;
a = *out
Load *in
Load *out
branch
*in cached
*in not cached
Load *in
Load *out
branch
Delay
Delay

## Slide 15: Weird NOT gate
Assume
*in == 0
Branch mispredicted
if (*in == 0)
return;
out *= 1;
out *= 1;
a = *out
Load *in
Delay
Load *out
branch
Load *in
Delay
Load *out
branch
*in cached
*in not cached
*in | *out
TRUE | FALSE
FALSE | TRUE
out  NOT(in)

## Slide 16: Thinking about this
Chains
Load *in
Delay
Load *out
branch
Signal
Probe
Control
Delay

## Slide 17: Combining Chains
if (*in1 + *in2 == 0)
return;
out *= 1
a = *out
Load *in1
Load *in2
Delay
Load *out
branch
*in1 | *in2 | *out
FALSE | FALSE | TRUE
FALSE | TRUE | TRUE
TRUE | FALSE | TRUE
TRUE | TRUE | FALSE
out  NAND(in1, in2)

## Slide 18: Multiple control chains
if (*in1 == 0)return;
if (*in2 == 0)return;
out *= 1
a = *out
Load *in2
branch
Delay
Load *out
Load *in1
branch
*in1 | *in2 | *out
FALSE | FALSE | TRUE
FALSE | TRUE | FALSE
TRUE | FALSE | FALSE
TRUE | TRUE | FALSE
out  NOR(in1, in2)

## Slide 19: Non-decreasing functions
if (delay()== 0)
return;
t1 = *in1
t2 = *in2;
a = *(out + t1 + t2)
Load *in1
Load *in2
Delay
Load *out
branch
*in1 | *in2 | *out
FALSE | FALSE | FALSE
FALSE | TRUE | FALSE
TRUE | FALSE | FALSE
TRUE | TRUE | TRUE
out  AND(in1, in2)

## Slide 20: OR gates (Adapted from Wang et al., WOOT 2023)
if (delay()== 0)
return;
a = *(out + *in1)
a = *(out + *in2)
Load *in1
Load *in2
Delay
Load *out
branch
*in1 | *in2 | *out
FALSE | FALSE | FALSE
FALSE | TRUE | TRUE
TRUE | FALSE | TRUE
TRUE | TRUE | TRUE
out  OR(in1, in2)
Load *out

## Slide 21: Replicator
if (delay()== 0)
return;
t = *in
a = *(out1 + t)
a = *(out2 + t)
Load *in
Delay
Load *out1
branch
Load *out2
...
a = *(outn + t)

## Slide 22: Composing more – multiple output NAND
if (*in1 + *in2 == 0)
return;
t = delay()
a = *(out1 + t)
a = *(out2 + t)
Load *in1
Load *in2
Delay
branch
Load *out1
Load *out2

## Slide 23: Minority Report
if (*in1 + *in2 == 0)
return;
if (*in2 + *in3 == 0)
return;
if (*in1 + *in3 == 0)
return;
a = *out
*in1 | *in2 | *in3 | *out
FALSE | FALSE | FALSE | TRUE
FALSE | FALSE | TRUE | TRUE
FALSE | TRUE | FALSE | TRUE
FALSE | TRUE | TRUE | FALSE
TRUE | FALSE | FALSE | TRUE
TRUE | FALSE | TRUE | FALSE
TRUE | TRUE | FALSE | FALSE
TRUE | TRUE | TRUE | FALSE

## Slide 24: Circuits
4-bit ALU
  1258 gates, 84-95% accuracy
SHA-1
  One round: 2208 gates, 95% accuracy (67% with prefetcher)
  Full (two blocks, with repetitions) 95% accuracy
Game of Life
  7807 gates 73% accuracy for one generation, 25% for 20

## Slide 25: The Flush+Reload Attack [YF14]
Flush a memory line from the cache
Wait a bit
Measure time to load line
  slow-> no access
  fast-> access
Repeat
Memory
Cache
Notes: Reminder: Fast 50 cycles. Slow 200. Measurement adds about 30 cycles.
Wrap-up – the weakness is that the spy can monitor access to shared memory lines and consequently infer information about the data the victim processes

## Slide 26: The RSA Encryption System
The RSA encryption is a public key cryptographic scheme
C = Me mod N
M
C
M = Cd mod N
Key Generation:
Select random primes p and q
Calculate N = pq
Select a public exponent e(=65537)
Compute d=e-1 mod φ(N)
(N, e) is the public key
(p, q, d) is the private key

## Slide 27: Square and Multiply Exponentiation
Operation | x | i | di
 | 1 | 2 | 101
Square | 1 | 2 | 101
reduce | 1 | 2 | 101
Multiply | 11 | 2 | 101
reduce | 11 | 2 | 101
Square | 121 | 1 | 101
reduce | 21 | 1 | 101
Square | 441 | 0 | 101
reduce | 41 | 0 | 101
Multiply | 451 | 0 | 101
reduce | 51 | 0 | 101
Example:
115 mod 100 =
161,051 mod 100 = 51
x ⟵1
for i ⟵|d|-1 downto 0 do
x ⟵x2 mod n
if (di = 1) then
x = xC mod n
endif
done
return x
The private key is encoded in the sequence of operations !!!
Notes: Old implementation – not in use

## Slide 28: Flush+Reload on Square-and-Multiply
40ns
Typical Clock Rates
Chrome 0.1ms
Safari 1ms
Firefox 2ms
TOR 100ms
Apple M1 42 ns

## Slide 29: Reducing Timer Resolution
Measure this
With this

## Slide 30: Amplification
A NOT gate with a large fan-out amplifies the signal by a factor of 8
  Two layers – 64
  Three layers – 512
  Four layers – 4096
Amplify to a resolution of 0.1 second
if (*in == 0)
return;
a = *out1 + *out2 +
*out3 + *out4 +
*out5 + *out6 +
*out7 + *out8;

## Slide 31: Amplification is half the job
40ns
25us

## Slide 32: Prime+Probe is NAND

## Slide 33: Prime+Probe is NAND

## Slide 34: Prime+Store: High Resolution Prime+Probe
Probe is basically a NAND gate
Do multiple probes of the same cache set. Store results.
Amplify later
  Decouples probing from time measurements
Attack square-and-multiply ElGamal with a 0.1ms clock

## Slide 35: How Fast can we Probe?

## Slide 36: How fast can we probe?
Probing the cache takes time
Limited temporal resolution
  Thousands of cycles
Prime+Scope (CCS 2021) – 70 cycles.

## Slide 37: Prime+Scope code
uint32_t scope(char * address) {
uint32_t start = rdtscp();
char t = *address;
uint32_t end = rdtscp();
return end – start;
}
30 cycles
30 cycles
5 cycles
5 cycles
Measuring time is an order of magnitude slower than a cache access

## Slide 38: Using Prime+Store
Prime+Store is a hammer – let’s try it on this nail.
Result: 150 cycles – branch training is not cheap

## Slide 39: Return-based gates (Kaplan 2023)
void NOTGate(char *out, char *in) {
setret(((uintptr_t)&&out) + *in);
out *= 1;
out *= 1;
t = *out;
lfence();
out:
}
setret:
mov %rdi, (%rsp)
ret
Load *in
Delay
Load *out
return

## Slide 40: Using Prime+Store
Prime+Store is a hammer – let’s try it on this nail.
Result: 150 cycles – branch training is not cheap
Prime+Store with RET-based gates: 48 cycles.
48 < 70 Yay!
48 is still very slow

## Slide 41: Timing analysis
void NOTGate(char *out, char *in) {
setret(((uintptr_t)&&out) + *in);
out *= 1;
out *= 1;
t = *out;
lfence();
out:
}
setret:
mov %rdi, (%rsp)
ret
+19 cycles for recovery from misprediction

## Slide 42: Tapped multi-probed gates
Load *in
Delay
Load *o3
return
Delay
Load *o2
Load *in
Load *in
Delay
Load *o2

## Slide 43: Tapped multi-probed gates
Load *in
Delay
Load *o3
return
Delay
Load *o2
Load *in
Load *in
Delay
Load *o2

## Slide 44: Tapped multi-probed gates
Load *in
Delay
Load *o3
return
Delay
Load *o2
Load *in
Load *in
Delay
Load *o2

## Slide 45: Gate operation time

## Slide 46: Gate resolution

## Slide 47: Results
For short runs, 5 cycles resolution
Sustained 10 cycles/probe, albeit non-uniform
Propose techniques for handling non-uniform probing
Demonstrate attacks on AES implementations

## Slide 48: Summary
Microarchitectural weird machines are a thing
Can have security impact
New emerging area – much work to do